## Slide 1: In-Flight Guide
388th Virtual Fighter Squadron
Current As Of (CAO):
2019-12-17
Version 1.2
Notes: Version 1.0: Initial version
Version 1.1: Added 3 Attackprofiles

## Slide 2: Authentication Table: AET-100
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Version 1.0 |  |  |  |  |  |  |  |  | 
 | A | B | C |  | D | E | F |  | G | H |  | I | J |  | K | L |  | M | N | O |  | P | Q | R |  | S | T | U |  | V | W |  | X | Y | Z
A | K | W | G |  | D | I | O |  | M | B |  | H | U |  | X | L |  | Z | E | A |  | J | F | R |  | N | V | S |  | T | C |  | Q | Y | P
B | J | A | R |  | N | B | E |  | G | C |  | O | Y |  | V | H |  | P | L | K |  | M | D | T |  | Z | Q | I |  | S | W |  | U | F | X
C | W | I | D |  | A | H | Z |  | E | K |  | L | M |  | R | F |  | N | J | U |  | O | V | G |  | X | S | T |  | C | Y |  | B | P | Q
D | B | A | T |  | F | D | J |  | I | G |  | Z | E |  | W | S |  | K | H | X |  | O | N | Y |  | P | R | L |  | U | M |  | Q | C | V
E | S | D | Z |  | J | X | P |  | B | E |  | M | Y |  | H | U |  | A | W | L |  | K | F | R |  | Q | C | G |  | T | N |  | V | I | O
F | L | I | A |  | W | F | D |  | E | H |  | K | Z |  | M | J |  | O | G | R |  | T | U | Q |  | V | N | X |  | P | S |  | Y | B | C
 | 0 |  |  |  | 1 |  |  |  | 2 |  |  | 3 |  |  | 4 |  |  | 5 |  |  |  | 6 |  |  |  | 7 |  |  |  | 8 |  |  | 9 |  | 
G | B | Y | T |  | C | S | Z |  | H | K |  | G | X |  | N | I |  | R | F | V |  | D | J | W |  | L | A | M |  | P | E |  | O | Q | U
H | H | F | B |  | Z | S | D |  | C | I |  | A | G |  | Y | K |  | R | L | P |  | U | M | V |  | N | Q | J |  | X | T |  | E | W | O
I | S | Z | M |  | D | O | C |  | G | H |  | F | I |  | P | T |  | N | K | R |  | J | A | W |  | V | E | Q |  | L | Y |  | U | X | B
J | R | E | L |  | Q | A | Z |  | K | I |  | T | H |  | F | O |  | X | G | W |  | D | Y | U |  | C | N | V |  | S | P |  | M | B | J
K | R | C | K |  | I | L | H |  | Q | T |  | U | S |  | Y | J |  | F | V | B |  | W | X | N |  | G | M | Z |  | P | E |  | O | D | A
L | Z | B | S |  | H | C | D |  | G | F |  | I | K |  | A | L |  | R | J | M |  | P | N | V |  | Q | Y | T |  | W | U |  | X | O | E
 | 0 |  |  |  | 1 |  |  |  | 2 |  |  | 3 |  |  | 4 |  |  | 5 |  |  |  | 6 |  |  |  | 7 |  |  |  | 8 |  |  | 9 |  | 
M | E | O | X |  | U | W | T |  | Y | Q |  | V | N |  | P | M |  | J | R | L |  | A | K | I |  | F | G | D |  | C | H |  | S | B | Z
N | I | F | G |  | D | C | H |  | S | B |  | Z | E |  | O | X |  | U | W | T |  | Y | Q | V |  | N | P | M |  | J | R |  | L | A | K
O | P | M | N |  | E | C | K |  | I | S |  | G | O |  | D | W |  | A | Y | Z |  | H | F | B |  | J | T | V |  | R | Q |  | X | U | L
P | N | V | Q |  | Y | T | W |  | U | X |  | O | E |  | Z | B |  | S | H | A |  | P | M | J |  | R | L | K |  | I | F |  | D | C | G
Q | G | D | F |  | C | I | H |  | K | S |  | A | B |  | L | Z |  | R | J | E |  | O | X | U |  | W | T | Y |  | Q | V |  | N | P | M
R | M | P | J |  | N | R | V |  | Z | Q |  | L | Y |  | B | T |  | S | W | H |  | U | A | K |  | X | C | O |  | G | D |  | E | F | I
 | 0 |  |  |  | 1 |  |  |  | 2 |  |  | 3 |  |  | 4 |  |  | 5 |  |  |  | 6 |  |  |  | 7 |  |  |  | 8 |  |  | 9 |  | 
S | B | H | D |  | F | E | X |  | W | Y |  | V | P |  | J | R |  | A | I | G |  | C | S | Z |  | O | U | T |  | Q | N |  | M | L | K
T | D | F | K |  | L | J | P |  | V | Y |  | W | X |  | E | Z |  | S | C | G |  | I | A | R |  | M | N | Q |  | T | U |  | O | B | H
U | M | P | N |  | D | Z | B |  | S | H |  | C | V |  | Q | Y |  | G | K | R |  | J | W | U |  | X | F | E |  | L | O |  | T | I | A
V | I | K | A |  | M | P | N |  | V | Q |  | L | R |  | J | Y |  | T | W | U |  | X | O | E |  | Z | B | S |  | H | C |  | D | G | F
W | D | G | F |  | I | W | B |  | Z | V |  | K | A |  | L | S |  | H | C | R |  | J | M | P |  | Q | Y | T |  | O | E |  | U | X | N
X | A | L | R |  | J | M | F |  | Z | B |  | S | Q |  | C | D |  | I | K | G |  | H | W | U |  | P | N | V |  | E | Y |  | T | O | X
Y | T | M | P |  | N | B | S |  | H | C |  | W | U |  | X | K |  | I | A | L |  | R | J | O |  | E | Z | V |  | Q | Y |  | D | G | F
 | 0 |  |  |  | 1 |  |  |  | 2 |  |  | 3 |  |  | 4 |  |  | 5 |  |  |  | 6 |  |  |  | 7 |  |  |  | 8 |  |  | 9 |  | 
AET = Authentication Encryption Table |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
COMPLEXITY (Uneven) LUMBERJACK (Even)

## Slide 3: STARTUP 1 / 4
GROUND POWER………………………………............ | CONNECT
SKIN, BORT, LOADOUT, FUEL .................................. | SET
INTERNAL LIGHTS ..................................................... | SET
AIR SOURCE | NORM
FUEL MASTER ............................................................ | ON – GUARDED
ENGINE FEED ............................................................. | NORM
EPU .............................................................................. | NORM – GUARDED
ENG CONT ................…….………............................... | PRI – GUARDED
THROTTLE .................................................................. | OFF
LANDING GEAR ....….…….......................................... | DOWN and LOCKED
HOOK ...………………………….………………............. | UP
MASTER ARM ...……………..………………………….. | SAFE (OFF)
MAIN PWR ................................................................... Verify FLCS RLY light ON | BATT
FLCS PWR TEST ........................................................ Verify ACFT BATT TO FLCS, FLCS PMG & FLCS PWR (4) lights ON | TEST - HOLD
MAIN PWR ................................................................... Verify ELEC SYS, HYD/OIL PRESS, FLCS RLY, SEC & ENGINE lights ON | MAIN PWR
EPU GEN & EPU PMG lights ..................................... | Confirm OFF
EXTERIOR LIGHTS……………………………………… | POSITION LIGHT- FLASH
MASTER COVER KNOB ............................................. | NORM
C&I KNOB………………………………………………… | BACKUP
AUDIO PANEL 1&2……………………………………… | AS REQUIRED
UHF BACKUP……………………………………............ | SET & CHECK-IN
AVIONICS…………………………………………………MMC, ST STA, MDF, UHF, GPS | ON
INS TO ALIGN……………………………………………. | ALIGN NORM

## Slide 4: STARTUP 2 / 5
MIDS LVT ....................................................................... | ON
FLIGHT CLOCK…………………………………………… | START
L&R HARDPOINT………………..……………………….. | AS REQ
FCR………………………………..………………………… | ON
RADAR ALTIMITER……………..……………………….. | STBY
DED INS…………………………..………………………… | ENTER DATA
HUD………………………………..………………………... | AS REQ
C&I………………………………..…………………………. | UFC
IFF ...........................……………..………………………... | SET & STANDBY
*DTC………………………………..……………………….. | LOAD
CAT 1 / CAT 3 | AS REQ
UFC RADIO……………………..…………………………. | SET & CHECK-IN
ATIS | CHECK
AVIONICS PROGRAM | 
SELECTIVE JETTISON ................................................. | SET
SMS ................................................................................ | PROGRAM
MSL & ALOW ................................................................ | SET
BINGO……………………………………..……………….. | SET JOKER
*CRUISE……………………………………..……………... | CHECK
TACAN…………………………………………..………….. | PREP
*IDM……………………………………………..…………... | CHECK
BULLSEYE……………………………………………….... | CHECK
STEERPOINTS…………………………………………….. | PROGRAM
EGI CHECK ALIGNED………………………………….... | SET NAV
REPORT READY………………………………………….. | ALPHA CHECK & ENGINE START

## Slide 5: STARTUP 3 / 5
CANOPY……………………………………………………. | LOCKED
JFS TO START 2…………………………………………... | VERIFY LIGHT
RPM 20%........................................................................ | THROTTLE TO IDLE
RPM 55%........................................................................ | VERIFY JFS OFF
RPM 60%........................................................................ | VERIFY ENG. WARN OFF
RPM 15-70%.................................................................. | VERIFY HYD/OIL OFF
ENGINE IDLE CHECK……………………………………. | 
FUEL FLOW……………………………………………….. | 700-1700 PPH
OIL PRESSURE…………………………………………… | MIN 15 PSI
NOZZLE POSITION……………………………………….. | > 94%
RPM…………………………………………………………. | 62-80%
FTIT………………………………………………………….. | < 650 DEGRESS C
HYD PRESSURE A&B……………………………………. | 2850-3250
AFTER START……………………………………………... | 
GROUND POWER………………………………………… | DISCONNECT
TESTS………………………………………………………. | PROBE, FIRE MAL& IND
FLIGHT CONTROLS……………………………………… | CYCLE & FREE
FLCS ……………………………………………………….. | RUN BIT
SPEED BRAKE……………………………………………. | CYCLE
RWR &CMDS………………………………………………. | ON / TEST/ STANDBY
HMDS ………………………………………………………. | ON &STOW
NVG…………………………………………………………. | PREP & STOW
FUEL QUANTITY………………………………………….. | TEST & SET NORM
EPU FUEL QUANTITY……………………………………. | 95-102%
AIR REFUEL SWITCH……………………………………. | CYCLE & CHECK
BACKUP ADI………………………………………………. | UNCAGE

## Slide 6: STARTUP 2 / 4
ENGINE START | 
CANOPY………………. | LOCKED
JFS TO START 2…….. | VERIFY LIGHT
RPM 20%..................... | THROTTLE TO IDLE
RPM 55%..................... | VERIFY JFS OFF
RPM 60%..................... | VERIFY ENG. WARN OFF
RPM 15-70%................ | VERIFY HYD/OIL OFF
ENGINE IDLE CHECK | 
FUEL FLOW………….. | 700-1700 PPH
OIL PRESSURE……… | MIN 15 PSI
NOZZLE POSITION…. | > 94%
RPM……………………. | 62-80%
FTIT……………………. | < 650 DEGRESS C
HYD PRESSURE A&B… | 2850-3250
AFTER START | 
GROUND POWER…… | DISCONNECT
TESTS…………………. | PROBE, FIRE MAL& IND
FLIGHT CONTROLS… | CYCLE & FREE
FLCS…………………... | RUN BIT
SPEED BRAKE………. | CYCLE
RWR &CMDS…………. | ON / TEST/ STANDBY
HMDS………………….. | ON &STOW
NVG……………………. | PREP & STOW
FUEL QUANTITY………. | TEST & SET NORM
EPU FUEL QUANTITY… | 95-102%
AIR REFUEL SWITCH | CYCLE & CHECK
BACKUP ADI…………… | UNCAGE
FLIGHT CLOCK…….. | START
L&R HARDPOINT….. | AS REQ
FCR…………………… | ON
RADAR ALTIMITER... | STBY
DED INS……………… | ENTER DATA
HUD…………………... | AS REQ
C&I……………………. | UFC
IFF MASTER KNOB.. | SET&STANDBY
*DTC…………………. | LOAD
CAT 1 / CAT 3……….. | AS REQ
UFC RADIO…………. | SET & CHECK-IN
ATIS…………………... | CHECK
AVIONICS PROGRAM | 
SELECTIVE JETTISON | SET
SMS…………………... | PROGRAM
ALOW………………… | SET
MSL…………………... | SET
BINGO……………….. | SET JOKER
*CRUISE……………... | CHECK
TACAN……………….. | PREP
*IDM…………………... | CHECK
BULLSEYE………….. | CHECK
STEERPOINTS……… | PROGRAM
EGI CHECK ALIGNED……………. | SET NAV
REPORT READY…… | ALPHA CHECK & ENGINE START

## Slide 7: STARTUP 3 / 4
DBU CHECK | 
DIGITAL BACKUP SW…………………………… | BACKUP
DBU ON WARNING LIGHT……………………… | CHECK ON
OPERATE CONTROLS…………………………... | CHECK RESPONSE
DIGITAL BACKUP SW…………………………… | OFF
DBU ON WARNING LIGHT……………………… | CHECK OFF
TRIM CHECKS | 
TRIM AP DISC SW………………………………... | DISC
STICK TRIM BUTTONS ACTION……………….. | CHECK NO RESPONSE
TRIM AP DISC SWITCH ………………………… | NORM
STICK TRIM BUTTONS………………………….. | CHECK INDICATORS & CENTRE
RUDDER TRIM CHECK………………………….. | CHECK AND CENTER
EPU CHECK | 
EPU GEN AND EPU PMG LIGHTS…………….. | CHECK OFF
OXYGEN…………………………………………… | SET 100%
TOE BRAKES……………………………………... | ENGAGE
EPU SWITCH……………………………………… | OFF THEN NORM
THROTTLE ……………………………………….. | SET 80%
EPU/GEN TEST SW……………………………… | EPU/GEN AND HOLD
EPU AIR LIGHT…………………………………… | VERIFY ON
EPU GEN AND EPU PMG LIGHTS…………….. | VERIFY OFF
FLCS POWER…………………………………….. | ON
VERIFY EPU RUN LIGHT ON…………..………. | WITHIN 5 SECONDS
EPU GEN TEST SW……………………………… | OFF (RELEASE)
THROTTLE ……………………………………….. | IDLE
OXYGEN…………………………………………… | NORM

## Slide 8: STARTUP 4 / 4
BEFORE TAXI | 
ALTIMITER………………………………………… | SET
INS………………………………………………….. | CHECK NAV
TGP…………………………………………………. | CHECK STOWED
MFD’S………………………………………………. | AS REQ
GROUND CREW………………………………….. | CHECK CLEAR
POSITION LIGHTS | STEADY
REPORT……………………………………………. | READY TAXI
TAXI BRIEF (FLIGHT LEAD)………………….... | COMPLETE
NOSE WHEEL STEERING………………………. | ON
TAXI LIGHTS | ON
BRAKES …………………………………………... | CHECK
HOLD SHORT | 
PROBE HEAT……………………………………... | ON
TRIM ……………………………………………….. | AS REQ
IFF…………………………………………………... | NORM
ENGINE CONT……………………………………. | VERIFY PRI
SPEED BRAKE…………………………………… | CLOSED
EJECTION SEAT…………………………………. | ARM
TACAN …………………………………………….. | ON
RADAR ALTIMITER……………………………… | ON
EXTERNAL TANKS………………………………. | VERIFY FEEDING
FLIGHT CONTROL………………………………. | FREE & CLEAR
OIL PRESSURE…………………………………… | CHECK PSI
TAKE OFF BRIEF (FLIGHT LEAD)…………….. | COMPLETE
ANTI COLLISION & LANDING LIGHT | ON (LINE UP)

## Slide 9: NORMAL OPERATIONS
TAKE OFF | 
WIPEOUT…………... | CLEAR
RPM…………………. | 90%
ENG. CHECK………. | GREEN
NWS…………………. | OFF (70KTS)
CLIMB OUT | 
GEAR……………….. | UP
ENGINE ……………. | GREEN
FUEL………………… | CHECK FEED
LANDING LIGHT….. | OFF
DRIFT CO…………... | AS REQ
BACKUP AVIONICS. | CHECK
AAR: BEFORE = DOWN / AFTER = UP | 
MASTER ARM……... | SAFE/AS REQ
LASER ARM……….. | SAFE/AS REQ
SMS…………………. | VERIFY
CMDS……………….. | OFF/ON
TACAN……………… | AS REQ
EMITTERS…………. | AS REQ
RADAR..................... | AS REQ
LIGHTS..................... | AS REQ
REFUEL DOOR........ | OPEN/CLOSED
DECENT | 
FUEL CHECK………….. | BALANCE
LANDING LIGHT……… | ON
SWITCHES…………….. | SAFE
TGP……………………... | STOW
ATIS……………………... | CHECK
ILS/TACAN…………….. | PROGRAM
CRS/HDG………………. | SET
FINAL SPEED…………. | COMPUTE
CLEAR COMPLETE | 
PROBE HEAT…………. | OFF
ECM PWR……………… | OFF
SPEED BRAKES……. | CLOSED
EJECTION SEAT ……... | SAFE
IFF………………………. | STBY
LANDING LIGHTS …… | TAXI
ANTI COLLISION……... | OFF
SHUTDOWN | 
EGI………………………. | OFF
AVIONICS……………… | OFF
THROTTLE…………….. | OFF
JFS RUN LIGHT………. | CHECK
EP GEN/EPU PMG……. | OFF
MAIN PWR……………... | OFF
OXYGEN……………….. | OFF
CANOPY……………….. | OPEN

## Slide 10: COMBAT OPERATIONS
FENCE | 
MASTER MODE…… | AS REQ
MASTER ARM……... | ARM
RADAR……………… | AS REQ
TACAN……………… | AS REQ
LASER ARM……….. | AS REQ
CHAFF/FLARES…... | SET
* ECM JAMMER…… | AS REQ
RWR………………… | CHECK ON
HMDS……………….. | ON
IR COOL……………. | SET
TGP………………….. | AS REQ
AGM65 PWR……….. | AS REQ
A-G WEAPONS……. | CHECK RELEASE PARAMTERS
THREAT&MSL VOLUME……………. | SET
STORES CONFIG…. | CONFIG
LIGHTS……………... | AS REQ
A-G CHECK | 
A-G MODE……….. | SELECT
MASTER ARM…… | ARM
LASER ARM……... | AS REQ
ORDNANCE……… | SELECTED
PROFILE…………. | SET
CMDS …………….. | SET
SOI / SPI………….. | SET
CCIP / CCRP…….. | AS REQ
ATTACK BRIEF….. | COMPLETE
EGRESS | 
OPS CHECK……... | PERFORM
BUDDY CHECK…. | PERFORM
BDA/INFLIGHT REP……………….. | TRANSMIT

## Slide 11: ATTACK PROFILES

## Slide 12: Check-list: Before Engine Start (cont)
CANOPY ........................................... | CLOSED – LOCKED
NOTE: To prevent preserve battery, do not allow MAIN PWR to remain in BATT or MAIN PWR for more than 5 minutes without engine start. | 
Check-list: Starting Engine
JFS .................................................... Check JFS light ON. | START 2
THROTTLE ....................................... Requires minimum 20% RPM minimum | IDLE
SEC Caution Light ........................... Above 20% RPM | Check OFF
ENGINE Warning Light ................... Above 60% RPM | Check OFF
JFS .................................................... Snaps OFF at 55% RPM | Check OFF
HYD/OIL PRESS light …...……….... Between 15% and 70% RPM | Check OFF
NOTE: Engine light-off occurs within 10 seconds after throttle advance and is indicated by an increase in RPM, followed by an increase of FTIT. Without external power connected, only the RPM and FTIT indicators function until the standby generator is online. | 
ENGINE CHECK AT IDLE FUEL FLOW......................................................... 700 – 1700 PPH OIL Pressure MIN 15 PSI NOZ POS >94% RPM 62-80% FTIT < 650 degs C HYD PRESS A&B 2850 – 3250 psi (around 12 o’clock) | 

## Slide 13: After Engine Start
TEST switch panel .......................... Probe Heat Fire and Overheat Detect MAL & IND | CHECKED
AVIONICS POWER .......................... MMC (FCC), ST STA (SMS), MFD, UFC, DL (MAP), GPS | ON
INS .................................................... | ALIGN NORM
SENSOR PANEL .............................. LEFT HDPT – OFF (unless required) RIGHT HDPT – As required FCR – FCR RDR ALT - STBY | SET
HUD PANEL ..................................... HYD SYM WHEEL – ON | AS REQUIRED
C&I .................................................... | UFC
DTC ................................................... | LOAD
UFC RADIO ...................................... | SET & CHECK IN
MFL ................................................... | RESET
SEC CHECK ..................................... | PERFORM
FLIGHT CONTROLS ........................ | CYCLE & CHECK
FLCS BIT .......................................... | CONDUCT
SPD BRK .......................................... | CYCLE
GEAR LEVEL ................................... | CHECK
FUEL QTY SEL ................................ | SET
EPU FUEL QTY ................................ | 95 – 102%

## Slide 14: After Engine Start (cont)
AVIONICS ......................................... THREAT WARNING AUX: ON CMDS: RWR: ON JMR: ON CHAFF & FLR CMDS: ON MODE: AS REQ’D PGRM: AS RQ’D ECM: AS REQUIRED THREAT WARNING PRIME HANDOFF: DIAMND FLT MFD: S-JETTISON: PRESET AND EXIT MASTER MODE: CONFIGURE SMS DED – UFC: ALOW – MSL – BINGO: CHECK CRUS – TACAN – IDM: CHECK BULLSEYE: SET & MODE SELECTED | PROGRAM
DBU CHECK ..................................... DIGITAL BACKUP SW: BACKUP DBU ON WARNING LIGHT: CHECK ON OPERATE CONTROLS: CHECK RESPONSE DIGITAL BACKUP SW: OFF DBU ON WARNING LIGHT: CHECK OFF | COMPLETED
TRIM CHECKS ................................. TRIM AP DISC SW: DISC STICK TRIM BUTTONS: ACTION CHECK NO RESPONSE TRIM AP DISC SWITCH: NORM STICK TRIM BUTTONS: CHECK AND CENTRE CONTROL SURFACE & INDICATOR MOTION RUDDER TRIM CHECK: YAW TRIM KNOB CHECK AND CENTER | COMPLETED
AIR REFUEL SWITCH ..................... | CYCLE & CHECK
EPU CHECK ..................................... EPU GEN and EPU PMG LIGHTS: OFF O2: 100% TOE BRAKES: ENGAGE EPU SWITCH: OFF | COMPLETED

## Slide 15: After Engine Start (cont)
EPU CHECK ..................................... EPU SWITCH: NORM THROTTLE: SET 80% EPU/GEN TEST SW: EPU/GEN AND HOLD CHECK LIGHTS: EPU AIR ON EPU GEN and EPU PMG OFF FLCS PWR ON EPU RUN ON (within 5s) EPU/GEN TEST SW: OFF (release) THROTTLE: IDLE O2: NORMAL | COMPLETED
OBOGS ............................................. OBOGS BIT SW: BIT VERIFY LIGHT: OXY LOW ON (for 10s) THEN OFF PRESSURE: CHECK 25-40 PSI MODE LEVER: PBG/ON (as req’d) DILUTER LEVER: NORM EMERGENCY LEVER: NORM FLOW INDICATOR: CHECK | CHECKED

## Slide 16: Check-list: Taxi, Takeoff
BEFORE TAXI | 
ALTIMETER ................. | SET
INS ............................... | CHECK - NAV
DDIS ..…………..…..… | SET
TACAN ........................ | SET
FORM LIGHTS ............ | AS REQ’D
CANOPY ...................... | CLOSED
PARKING BRAKE ....... | STOWED
NWS ............................. | ON
LANDING LIGHT ......... | ON
BRAKES ...................... | CHECK
SWING CHECK ........... | COMPLETE
HOLD SHORT | 
EJECTION SEAT ......... | ARM
PROBE HEAT .............. | PROBE HEAT
TACAN …..................... | ON & CHECK
ANTI COLLISION LT ... | BRIGHT
MANUAL TF FLY UP ... | ENABLE
TRIMS .......................... | CENTRE
ENG CONT .................. | PRI
SPEEDBRAKE ............ | CLOSED
DEP. CLEARANCE ...... | RECEIVED
RADAR ALTIMETER ... | ON
HOLD SHORT (CONT) | 
STORES CONFIG SW . | AS REQ’D
GND JET ENBL SW.. | AS REQ’D
EXTNL TANKS ......... | CHECK
FLT. CONTROLS ...... | FREE & CLEAR
OIL PRESSURE ....... | CHECK PSI
TAKE OFF | 
WIPEOUT CHECK ... | CLEAR
RPM .......................... | 90%
ENGINE CHECK ...... | GREEN
BRAKES ................... | RELEASE
NWS ......................... | OFF (70kts)
CLIMB OUT | 
LANDING LIGHT ...... | OFF
LANDING GEAR ...... | CHECK UP
ENGINE .................... | IN GREEN
FUEL ......................... | CHK FEEDING
DED ........................... | SET
DRIFT CO ................. | SET DRIFT
AVIONICS ................. | CHECK

## Slide 17: Check-list
CRUISE | 
OPS CHECK…..… | PERFORM
RADAR.…..………. | SET
ECM….………....… | BIT/ON
CMS……...……….. | PROGRAM
RADIOS….……… | SET
INGRESS | 
OPS CHECK……... | PERFORM
RAD ALT……....…. | SET
EMCON……...……. | AS REQ’d
BINGO/JOKER…... | VERIFY/SET
RADIOS.………..… | AS REQ’d
C2 report…………. | Report
FENCE | 
TCN…................... | AS REQ’d
RADAR……………. | AS REQ’d
MASTER ARM..….. | ARM
CMDS/ECM…….… | SET
RWR volume…….. | SET
Stores Jettison | SET
Lights | SET
A-G Check | 
Attack brief | Complete
TGT designate.…. | CHECK
Master Arm........… | ARM
AG MODE..……….. | SELECT
Weapon select…... | CLEAR
ECM/CMDS………. | ARMED
EGRESS | 
OPS CHECK……… | PERFORM
BUDDY CHECK….. | PERFORM
BINGO…….………. | OFF 250 Kts
RADIOS………..…. | OFF
BDA / Inflight rep | TRANSMIT
AAR | 
MASTER ARM | SAFE
RADAR | SILENT
TACAN | OFF
LIGHTS | AS REQ’d
DDIS | AS REQ’d
Fuel Feed | AS REQ’d
NOT UPDATED for VIPER

## Slide 18: Check-list
DECENT | 
MASTER ARM | SAFE
Anti Ice……...….. | AS REQ’d
Pitot heat.………. | AUTO
DEFOG.………....… | HIGH
WindshieldAnti Ice | AS REQ’d
STBY Instruments. | CHECK
TCN ……................ | SET
ICLS…….……....…. | SET
Anti Skid…...……. | SET
Hook bypass...…... | SET
Radar Alt………..… | SET
LAND | 
HOOK................... | SET
Landing lights…. | AS REQ’d
NOT UPDATED for VIPER

## Slide 19: Check-list: SCRAMBLE
Skin, Bort…… | SET
Loadout…… | SET
Battery................. | ON
APU………........... | ON
INS..……………… | ALIGN
NAV LIGHT…….. | ON
Engine crank. | RIGHT
Right Throttle… | IDLE
Engine crank… | LEFT
Left Throttle…... | IDLE
EMI/IFEI …… | CHECK
LDDI/RDDI…… | ON & SET
MPCD & HUD…… | ON & SET
Bleed Air | CYCLE
Radios | AS REQ’d
FCS | RESET
OBOGS | ON
INS | NAV/IFA
NWS | ENGAGED
Park brakes | STOWED
TAXI | 
Ejection seat…… | ARMED
Straps................. | TIGHT
TACAN…............. | SET & ON
RWR …………….. | ON
RADAR………….. | OPER
Dispencer………. | ON
Selective Jett…... | SET
TAKEOFF | 
Rolling takeoff Full AB Climb/Course – As Required | 
FENCE IN | 
RADAR | ON
Mastermode | A-A
IR Cooler | ON
ECM | AS REQ’d
RWR | ON
Master Arm | ARM
Lights | AS REQ’d
NOT UPDATED for VIPER

## Slide 20: Presets ATRM v1.0
COMM 1 - UHF |  |  |  | COMM 2 -VHF |  |  | 
1 | 310.0 |  | Internal PRI | 1 |  |  | Internal SEC
2 | 237.0 | BLUE 3 | Check-in | 2 | 126.1 |  | Al Dahfra GND
3 | 228.0 | ORANGE10 | A-A #1 | 3 | 126.2 |  | Al Dahfra TWR
4 | 249.0 | GREEN4 | A-G#1 | 4 | 127.1 |  | Al Dahfra CNTRL
5 | 234.0 | OCHRE 9 | Inflight report | 5 | 136.25 | INDIGO6 | AWACS backup
6 | 242.5 | OCHRE 4 | Range 1 | 6 | 132.75 | LEMON3 | Range 3 SEC
7 | 239.75 | INDIGO 4 | Range 2 | 7 | 120.25 | OCHRE5 | Range 4 SEC
8 | 243.75 | CHERRY 8 | Range 3 | 8 | 136.75 | OCHRE 8 | Range 5 SEC
9 | 225.75 | INDIGO 10 | Range 4 | 9 | 139.75 | AQUA10 | Range 6 SEC
10 | 235.75 | AMBER 4 | Range 5 | 10 | 130.7 | YELLOW 6 | Range 9 SEC
11 | 233.25 | BROWN 7 | Range 6 | 11 | 151.0 | AR201 | ARCO
12 | 234.75 | PINK 7 | Range 7 | 12 | 144.0 | AR402 (R) | ARCO (RED)
13 | 230.5 | INDIGO 11 | Range 8 | 13 | 143.0 | AR403 (R) | ARCO (RED)
14 | 236.5 | LEMON 7 | Range 9 | 14 | 150.0 | AR101 | ARCO
15 | 245.0 | RED 5 | Range10 | 15 | 118.2 | TWR | Ras Al Kaimah(R)
16 | 228.75 | GRAY 5 | Range 11 | 16 | 124.2 | TWR | Khasab (R)
17 | 242,25 | ORANGE 2 | Range 12 | 17 | 128.2 | TWR | Sas Al Nakheel(R)
18 | 235.0 | WHITE 11 | MOA 1 | 18 | 119.2 | TWR | Al Ain
19 | 246.25 | ORANGE 7 | MOA 2 | 19 | 121.2 | TWR | Al Minhad
20 | 230.0 | YELLOW 6 | MOA 3 | 20 | 119.6 | TWR | Liwa

## Slide 21: Presets TRM v1.1
COMM 1 |  |  |  | COMM 2 |  |  | 
1 | 230.250 | GREEN 5 | Internal | 1 | 134.1 |  | Kutaisi GND
2 | 234.500 | PINK 9 | Internal | 2 | 134.2 |  | Kutaisi TWR
3 | 245.250 | LIME 8 | Internal | 3 | 127.1 |  | Kutaisi CNTRL
4 | 239.000 | CORAL 9 | Internal | 4 | 237.000 | BLUE 3 | AWACS Check-in
5 | 227.750 | OCHRE 1 | Internal | 5 | 228.000 | ORANGE 10 | AWACS A-A #1
6 | 248.250 | BROWN 1 | Internal | 6 | 248.000 | GRAY 2 | AWACS A-A #2
7 | 230.750 | LIME 5 | Tanker A | 7 | 228.250 | VIOLET 10 | SCRAMBLE Freq
8 | 235.500 | GOLD 7 | Tanker B | 8 | 234.000 | OCHRE 9 | Inflight Report Net
9 | 234.000 | OCHRE 9 | Inflight Report Net | 9 | 245.000 | RED 5 | RANGE CONTROL
10 | 230.000 | YELLOW 6 | MOA WEST | 10 | 230.000 | YELLOW 6 | MOA WEST
11 | 242.250 | ORANGE 2 | MOA CENTER | 11 | 242.250 | ORANGE 2 | MOA CENTER
12 | 228.750 | GRAY 5 | MOA EAST | 12 | 228.750 | GRAY 5 | MOA EAST
13 | 242.500 | OCHRE 1 | Range 1 | 13 | 242.500 | OCHRE 1 | Range 1
14 | 239.750 | INDIGO 4 | Range 2A | 14 | 239.750 | INDIGO 4 | Range 2A
15 | 225.750 | INDIGO 10 | Range 3A | 15 | 225.750 | INDIGO 10 | Range 3A
16 | 235.750 | AMBER 4 | Range 3B | 16 | 235.750 | AMBER 4 | Range 3B
17 | 233.250 | BROWN 7 | Range 4A | 17 | 233.250 | BROWN 7 | Range 4A
18 | 234.750 | PINK 7 | Range 4B | 18 | 234.750 | PINK 7 | Range 4B
19 | 228.250 | VIOLET 10 | SCRAMBLE FREQ | 19 | 134.4 |  | Kutaisi PAR
20 | 243.0 |  | GUARD | 20 | 243.0 |  | GUARD
NOT UPDATED for VIPER

## Slide 22: Presets OPUF
COMM 1 |  |  |  | COMM 2 |  |  | 
1 | 247.000 | GOLD1 | Internal | 1 | 126.1 |  | Al Dahfra GND
2 | 227.750 | OCHRE1 | Internal | 2 | 126.2 |  | Al Dahfra TWR
3 | 246.000 | LIME3 | Internal | 3 | 126.9 |  | Al Dahfra CNTRL
4 | 226.500 | MAROON10 | Internal | 4 | 231.500 | GREEN 7 | AWACS Check-in
5 | 241.000 | MAROON 8 | Internal | 5 | 248.000 | GREY 2 | A-A #1
6 | 225.500 | CORAL 11 | Internal | 6 | 229.000 | GREEN 4 | A-A #2
7 | 225.750 | INDIGO 10 | Internal | 7 | 235.250 | GREY 6 | A-G #1
8 | 244.250 | CHERRY 11 | Internal | 8 | 234.500 | PINK 9 | A-G #2
9 | 233.750 | AQUA 8 | Internal | 9 | 122.250 | GRAY 10 | VHF backup
10 | 239.250 | CHERRY 9 | Internal | 10 | 228.000 | ORANGE 10 | In flight report net
11 | 247.500 | LIME 11 | Tanker SHELL | 11 | 233.000 | PINK 1 | CSAR Net
12 | 240.750 | MAROON7 | Tanker ARCO | 12 | 230.750 | LIME 5 | Package #1
13 | 119.250 | RED 11 | JTAC WARRIOR | 13 | 245.500 | GOLD 11 | Package#2
14 | 136.750 | OCHRE 8 | JTAC SPARTAN | 14 | 234.250 | LEMON 9 | Package #3
15 | 227.500 | YELLOW 1 | SCAR #1 | 15 | 121.1 |  | Al Minhad GND
16 | 235.000 | WHITE 11 | SCAR #2 | 16 | 121.2 |  | Al Minhad TWR
17 | 238.000 | PINK11 | SCAR #3 | 17 | 280.7 |  | CVN-74 Stennis ATC
18 | 300.0 |  | Backup | 18 | 280.9 |  | CVN-74 Stennis LSO
19 | 248.750 | GREEN 6 | SCRAMBLE Freq | 19 | 248.750 | GREEN 6 | SCRAMBLE Freq
20 | 301.0 |  | Backup | 20 | 126.3 |  | Al Dahfra PAR
NOT UPDATED for VIPER

## Slide 23: Presets Caucasus Defender
COMM 1 |  |  |  | COMM 2 |  |  | 
1 | 245.250 | LIME 8 | HAWK PRI | 1 | 140.1 |  | VAZIANI GND
2 | 234.500 | PINK 9 | FALCON PRI | 2 | 140.2 |  | VAZIANI TWR
3 | 139.250 | MAROON1 | HAWK SEC | 3 | 127.2 |  | TBLISI APPROACH
4 | 230.75 | LIME 5 | SHELL | 4 | 237.0 | BLUE 3 | DARKSTAR CHECK-IN
5 |  |  |  | 5 | 136.250 | INDIGO 6 | DARKSTAR BACKUP
6 |  |  |  | 6 | 229.0 | GREEN 4 | A-A CONTROLLER
7 |  |  |  | 7 | 228.0 | ORANGE 10 | IN FLIGHT REPORT
8 |  |  |  | 8 |  |  | 
9 |  |  |  | 9 |  |  | 
10 |  |  |  | 10 |  |  | 
11 |  |  |  | 11 |  |  | 
12 |  |  |  | 12 |  |  | 
13 |  |  |  | 13 |  |  | 
14 |  |  |  | 14 |  |  | 
15 |  |  |  | 15 |  |  | 
16 |  |  |  | 16 |  |  | 
17 |  |  |  | 17 |  |  | 
18 |  |  |  | 18 |  |  | 
19 |  |  |  | 19 |  |  | 
20 |  |  |  | 20 |  |  | 
NOT UPDATED for VIPER

## Slide 24: Template format: Retasking brief
TASK / MISSION | 
LOCATION/ KILLBOX NAME AND STATUS | 
ENEMY SITUATION/ TARGET | 
THREAT | 
FRIENDLIES | 
JTAC/FAC(A)/SCAR (OPTIONAL) | 
ORDNANCE | 
REMARKS | 
Retasking brief is used from AWACS to retask a flight to a new, more important mission during an event.

## Slide 25: Template format: Fighter Check-in
Mission number | 
Number and type AC | 
Position and altitude | 
Ordnance | 
Time on station | 
Capabilities | 
Abort code | 
Fighter check-in is used by CAS flights to a JTAC/FAC(A) or from a AR flight to a SCAR flight

## Slide 26: Template format: Area of Operations update
GFC Intent for CAS | 
Threat | 
Target/Enemy | 
Friendly | 
Artillery | 
Clearance authority | 
Ordnance requested | 
Restrictions | 
Hazards | 
Remarks | 
AO update is used by JTAC/FAC(A) to give a situation update for CAS missions

## Slide 27: Template format: CAS brief
GAMEPLAN | 
Type of Control | 
BOT/BOC | 
Ordnance | 
Method | 
9 LINE | 
IP | 
Heading | 
Distance | 
Elevation | 
Target | 
Location | 
Mark | 
Friendlies | 
Egress | 
Remarks/Restrictions | 
Remarks | 
Restrictions | 
CAS brief provides targeting information during CAS missions.

## Slide 28: Template format: SCAR brief
Gameplan/Flow | 
Target description | 
Location | 
Elevation | 
Area weather | 
Current threat | 
Additional information | 
SCAR brief is used to coordinate AR flights and give necessary information to AR flights

## Slide 29: Template format: In Flight Report
132nd INFLTREP | INFORMATION
Callsign | 
Mission Number | 
Target Location | 
Time on Target | 
Results (BDA) | 
Remarks | 
In flight Report is used to provide BDA and situation updates to AWACS during a mission.

## Slide 30: Template format: Handover brief
132nd Battle handover brief | INFORMATION
(1) Friendly situation | 
(2) Threat update | 
(3) Enemy situation / targets | 
(4) Control Measures in effect | 
(5) Clearance authority (if applicable) | 
(6) Frequency and callsigns | 
Handoverbrief is used to brief either a new flight coming on station, assuming the task/role/responsibility of the flight on station or to brief the second element during YO-YO operations

## Slide 31: Transmission authentication: TAT-101
 |  |  |  |  |  |  |  |  |  |  |  |  |  | Version 1.0 |  |  | 
0000 |  |  | 0100 |  |  | 0200 |  |  | 0300 |  |  | 0400 |  |  | 0500 |  | 
0600 |  |  | 0700 |  |  | 0800 |  |  | 0900 |  |  | 1000 |  |  | 1100 |  | 
1200 |  |  | 1300 |  |  | 1400 |  |  | 1500 |  |  | 1600 |  |  | 1700 |  | 
1800 |  |  | 1900 |  |  | 2000 |  |  | 2100 |  |  | 2200 |  |  | 2300 |  | 
00 | - | AQ | 00 | - | SX | 00 | - | BE | 00 | - | QI | 00 | - | AW | 00 | - | MH
02 | - | QE | 02 | - | BU | 02 | - | ST | 02 | - | SO | 02 | - | QL | 02 | - | MD
04 | - | CE | 04 | - | ML | 04 | - | MW | 04 | - | BQ | 04 | - | CH | 04 | - | QW
06 | - | ZR | 06 | - | MZ | 06 | - | AD | 06 | - | AI | 06 | - | CV | 06 | - | ZN
08 | - | SY | 08 | - | CD | 08 | - | BI | 08 | - | SW | 08 | - | QC | 08 | - | AX
10 | - | BY | 10 | - | CF | 10 | - | SU | 10 | - | QD | 10 | - | ZJ | 10 | - | QT
12 | - | MT | 12 | - | BD | 12 | - | BA | 12 | - | QF | 12 | - | SM | 12 | - | MQ
14 | - | MY | 14 | - | CW | 14 | - | AO | 14 | - | CY | 14 | - | CO | 14 | - | SE
16 | - | QY | 16 | - | ZQ | 16 | - | BT | 16 | - | ZG | 16 | - | SD | 16 | - | BF
18 | - | MA | 18 | - | BL | 18 | - | CR | 18 | - | MR | 18 | - | ZD | 18 | - | QO
20 | - | AT | 20 | - | CI | 20 | - | QQ | 20 | - | AB | 20 | - | SP | 20 | - | ZX
22 | - | AY | 22 | - | BX | 22 | - | AG | 22 | - | AN | 22 | - | SK | 22 | - | MF
24 | - | MS | 24 | - | MU | 24 | - | SS | 24 | - | SV | 24 | - | QG | 24 | - | BC
26 | - | BO | 26 | - | SR | 26 | - | ZA | 26 | - | AU | 26 | - | BN | 26 | - | BS
28 | - | BP | 28 | - | AE | 28 | - | AA | 28 | - | MC | 28 | - | ZM | 28 | - | ZK
30 | - | AF | 30 | - | ZI | 30 | - | CP | 30 | - | ZB | 30 | - | AP | 30 | - | MN
32 | - | AH | 32 | - | QR | 32 | - | QP | 32 | - | ZU | 32 | - | SH | 32 | - | QH
34 | - | MP | 34 | - | BZ | 34 | - | QA | 34 | - | AS | 34 | - | ZC | 34 | - | CB
36 | - | SL | 36 | - | BR | 36 | - | QS | 36 | - | MX | 36 | - | SQ | 36 | - | BW
38 | - | CA | 38 | - | ZL | 38 | - | ZS | 38 | - | BB | 38 | - | SF | 38 | - | SZ
40 | - | CS | 40 | - | MJ | 40 | - | MO | 40 | - | QJ | 40 | - | CG | 40 | - | QZ
42 | - | MG | 42 | - | BG | 42 | - | BH | 42 | - | QK | 42 | - | SN | 42 | - | CJ
44 | - | QN | 44 | - | ZT | 44 | - | AJ | 44 | - | ZE | 44 | - | ZY | 44 | - | AL
46 | - | AC | 46 | - | AM | 46 | - | AK | 46 | - | SJ | 46 | - | QX | 46 | - | QV
48 | - | MV | 48 | - | SG | 48 | - | ZO | 48 | - | QU | 48 | - | ZH | 48 | - | CQ
50 | - | BM | 50 | - | ZF | 50 | - | SC | 50 | - | CX | 50 | - | ZW | 50 | - | MB
52 | - | SA | 52 | - | ZV | 52 | - | CK | 52 | - | CC | 52 | - | BV | 52 | - | QM
54 | - | CT | 54 | - | AR | 54 | - | CL | 54 | - | SI | 54 | - | CM | 54 | - | MK
56 | - | MI | 56 | - | BJ | 56 | - | CZ | 56 | - | BK | 56 | - | QB | 56 | - | SB
58 | - | ZP | 58 | - | AZ | 58 | - | MM | 58 | - | AV | 58 | - | CU | 58 | - | ME
TAT=Transmission Authentication Table |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 32: 132nd Frequencies
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 
Blue | 123.000 | 238.250 | 237.000 | 128.000 | 31.25 | 118.500 | 117.500 | 226.250 | 117.000 | 30.75 | 125.000 | Blue
Green | 30.00 | 45.00 | 120.000 | 229.000 | 230.250 | 248.750 | 231.500 | 32.25 | 137.750 | 123.750 | 32.50 | Green
Red | 140.250 | 31.00 | 35.25 | 127.100 | 245.000 | 30.50 | 231.250 | 118.000 | 134.100 | 243.500 | 119.250 | Red
Yellow | 227.500 | 128.100 | 237.750 | 34.00 | 121.250 | 230.000 | 121.100 | 225.000 | 31.75 | 133.000 | 121.750 | Yellow
Orange | 122.000 | 242.250 | 243.250 | 129.000 | 117.750 | 225.250 | 246.250 | 32.75 | 119.500 | 228.000 | 229.750 | Orange
Purple | 248.500 | 127.000 | 134.250 | 130.250 | 38.25 | 131.000 | 236.000 | 237.500 | 133.750 | 138.100 | 127.750 | Purple
White | 126.250 | 137.250 | 238.500 | 126.000 | 237.250 | 117.250 | 121.000 | 118.750 | 120.500 | 119.000 | 235.000 | White
Gray | 35.00 | 248.000 | 128.750 | 122.100 | 228.750 | 235.250 | 135.250 | 242.750 | 118.250 | 122.250 | 30.25 | Gray
Pink | 233.000 | 130.100 | 124.000 | 128.250 | 125.750 | 34.50 | 234.750 | 34.75 | 234.500 | 244.750 | 238.000 | Pink
Brown | 248.250 | 138.750 | 136.000 | 33.50 | 132.250 | 232 | 233.250 | 231.750 | 120.750 | 228.500 | 137.000 | Brown
Violet | 240.000 | 135.100 | 134.750 | 232.500 | 232.750 | 32.00 | 130.750 | 129.250 | 132.000 | 228.250 | 136.100 | Violet
Amber | 124.750 | 238.750 | 227.000 | 235.750 | 244.500 | 226.000 | 36.50 | 123.250 | 126.750 | 131.100 | 124.100 | Amber
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 
Aqua | 33.75 | 129.750 | 226.750 | 131.250 | 231.000 | 247.750 | 133.100 | 233.750 | 236.250 | 139.750 | 36.75 | Aqua
Cherry | 121.500 | 31.50 | 242.000 | 35.75 | 243.000 | 138.000 | 132.100 | 243.750 | 239.250 | 131.750 | 244.250 | Cherry
Gold | 247.000 | 134.000 | 240.500 | 129.100 | 36.25 | 229.250 | 235.500 | 241.500 | 127.250 | 35.50 | 245.500 | Gold
Coral | 124.250 | 33.25 | 138.250 | 240.250 | 135.750 | 241.750 | 33.00 | 139.100 | 239.000 | 229.500 | 225.500 | Coral
Indigo | 137.100 | 119.750 | 233.500 | 239.750 | 245.750 | 136.250 | 139.000 | 246.500 | 140.750 | 225.750 | 230.500 | Indigo
Lemon | 34.25 | 133.50 | 132.750 | 123.100 | 36.00 | 241.250 | 236.500 | 37.50 | 234.250 | 135.000 | 37.75 | Lemon
Lime | 247.250 | 126.100 | 246.000 | 244.000 | 230.750 | 37.00 | 232.250 | 245.250 | 38.75 | 130.000 | 247.500 | Lime
Maroon | 139.250 | 38.00 | 239.500 | 122.750 | 39.25 | 39.50 | 240.750 | 241.000 | 37.25 | 226.500 | 140.000 | Maroon
Ochre | 227.750 | 236.750 | 227.250 | 242.500 | 120.250 | 39.00 | 38.50 | 136.750 | 234.000 | 125.250 | 39.75 | Ochre
Olive | 140.100 | 246.750 | 141.000 | 141.750 | 141.100 | 150.000 |  | 149.0 | 141.250 | 151.000 |  | Olive
Black | 35.650 | 25.375 | 48.550 |  | 36.300 | 37.800 | 38.200 | 39.800 | 40.400 | 41.000 | 36.333 | Black
Bronze | 309.000 | 140.700 | 130.700 | 135.700 |  | 306.000 | 132.700 | 310.000 |  |  |  | Bronze
Copper |  | 134.700 |  | 141.700 | 310.900 | 309.500 |  |  | 307.000 | 133.700 |  | Copper
Silver | 131.700 | 305.000 | 310.500 | 308.000 |  |  | 136.700 |  | 142.700 | 309.900 |  | Silver
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 

## Slide 33: Contracts
TAXI:
Trail
LINEUP:
Echelon lineup (2ship)
3 in the slot (4ship)
TAKE-OFF / DEPARTURE /REJOIN
20 sec seperation
AB off at 300kts
350kts
Finger 4, #2 Left
CRUISE
350kts or M0.8 (what is lower)
Turns: 30˚ bank
RECOVERY
OHB
5 sec interval in the break
AIR COMBAT READINESS
450 Kts/M0.70 defensive Combat spread
500-1000ft vertical seperation
Energy sustaining turns
TARGETING
1: Lead, High, Left
2: Trail, Low, Right
3: Maintain SA; support

## Slide 34: A-A BVR Timeline
Merge
NLT Defend
NLT Abort
Assess targeted status
Shoot: FOX 3 , Crank
Meld and Sort: FL to flight: FLIGHT: Meld BRAA 190 25,25 thousand
Tactical /target range
NLT Commit
35
30
25
20
15
10
8
4 Assumptions:
Visual: meaning they have sight of the other fighter
No Joy: meaning they do not have a tally on any unknown or hostile aircraft
Naked: meaning the fighters are not spiked by hostile radars
Clean: meaning the fighter has no radar contacts
#2 report if this changes and it have not been picked up by lead.
  Radar:
    #1 High and far
    #2 Low and near
    Sorting:
    #1 : Left, Lead, High
    #2: Right, Trail, Low
  Brevity
  MELD: Cease radar sanitization and focus radar on single target. Set :
  Range to 40 NM
  Reduce to 80 degrees Azimuth

## Slide 35: Reference
BEAM
BEAM
HOT
FLANK
FLANK
NOTCH
NOTCH
PUMP
CRANK
CRANK
HOT
DRAG
Enemy’s relation to you
Your relation to enemy

## Slide 36: Lineups
Echelon
3 in the slot
4 in the slot
1
1
2
3
4
1
2
4
3
1
2
4
3

## Slide 37: Formations
Finger 4 - Left
Finger 4 - Right
Echelon Left
Echelon Right
Line Abreast / Combat Spread
3ship VIC
Diamond
2ship Wedge
Fighting Wing
30˚
60˚
3000ft-6000ft
30˚
60˚
500ft-3000ft
1
2
3
4
1
2
3
4
1
3
2
4
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
1
2
3
4
1
2
1
2

## Slide 38: Turns

## Slide 39: Turns page 1
TAC-Left 90˚
TAC-Right 45˚
TAC-Left 45˚
TAC-Right 90˚
1
2
1
2
1
2
1
2
1
2
1
2
1
2
1
2

## Slide 40: Turns page 2
Hook Left
Hook Right
Cross Turn
Shackle
1
2
1
2
1
2
1
2
1
2
1
2
1
2
1
2

## Slide 41: Knots and nautical miles
Knot | Nautical mile per minute | Knot | Nautical mile per minute
200 | 3.3 | 400 | 6.7
210 | 3.5 | 410 | 6.8
220 | 3.7 | 420 | 7.0
230 | 3.8 | 430 | 7.2
240 | 4.0 | 440 | 7.3
250 | 4.2 | 450 | 7.5
260 | 4.3 | 460 | 7.7
270 | 4.5 | 470 | 7.8
280 | 4.7 | 480 | 8.0
290 | 4.8 | 490 | 8.2
300 | 5.0 | 500 | 8.3
310 | 5.2 | 510 | 8.5
320 | 5.3 | 520 | 8.7
330 | 5.5 | 530 | 8.8
340 | 5.7 | 540 | 9.0
350 | 5.8 | 550 | 9.2
360 | 6.0 | 560 | 9.3
370 | 6.2 | 570 | 9.5
380 | 6.3 | 580 | 9.7
390 | 6.5 | 590 | 9.8

## Slide 42: Gross wheights, landing config flaps
NOT UPDATED for VIPER

## Slide 43: Pressure table conversion
Hektopascal (HPA) | Inches Mercury (InHg) |  | 
1013.25 | 29.92 | 1013.25 | 29.92
NOT UPDATED for TRM or OPUF

## Slide 44: Range frequencies
TO BE ADDED

## Slide 45: Countermeasures
Manual program |  |  |  |  |  | 
Program | Type | Chaff | Flare | Interval | Cycle | Amount
1 | RF SAM Old | 1 | 0 | 0.5 | 6 | 6 chaff
2 | RF SAM New | 2 | 0 | 0.25 | 10 | 20 chaff
3 | IR SAM | 0 | 1 | 0.75 | 10 | 10 flare
4 | IR Pre-emptive | 0 | 1 | 5 | 10 | 10 flare
5 | A-A Merge | 2 | 1 | 0.5 | 6 | 12chaff +6flare
6 | Wall dispense, panic | 0 | 1 | 0.25 | 6 | 6 flare
Automatic program |  |  |  |  |  | 
Program | Type | Chaff | Flare | Interval | Cycle | Amount
 | Old Generation SAM | 1 | 0 | 0.5 | 6 | 6 chaff
 | Current generation SAM | 2 | 0 | 0.25 | 10 | 20 chaff
 | IR SAM | 0 | 1 | 0.25 | 5 | 5 flare
Old RF SAM: SA-2, SA-3, SA-6
New RF SAM: SA-10, SA-11, SA-13, SA-15, SA-19 (Tunguska)
IR SAM:SA-9, SA-18 (MANPAD)
NOT UPDATED for VIPER

## Slide 46: Threats page 1
RADAR |  |  |  |  |  | 
RWR | Code | Name | Max Range | Max alt | Counter Program | Type
2 | SA-2 | Guideline |  |  | 1 | 
FS |  |  |  |  |  | TR
FF |  |  |  |  |  | SR
3 | SA-3 | GOA | 11,2 NM | 20500ft | 1 | 
LB |  |  |  |  |  | SR Flatface
FF |  |  |  |  |  | TR Low blow
6 | SA-6 | KUB | 19,2 NM | 33000ft | 1 | 
8 | SA-8 | GECKO | 7,5 NM | 21000ft | 1 | 
10 | SA-10 | GRUMBLE | 40 NM | 105000ft | 2 | 
CS |  |  |  |  |  | 
BB |  |  |  |  |  | 
11 | SA-11 | GADFLY | 20,2 NM | 45000ft | 2 | 
SD |  |  |  |  |  | 
13 | SA-13 | GOPHER | 2,8 NM | 15000ft | 3 | IR guided
15 | SA-15 | GAUNTLET | 6,5 NM | 26000ft | 2 | 
S6 | SA-19 | GRISON | 4 NM | 16000ft | 2 | Tunguska
NOT UPDATED for VIPER

## Slide 47: Threats page 2
RADAR |  |  |  |  |  | 
RWR | Code | Name | Max Range | Max alt | Counter | Type
HA | HAWK | HAWK | 25,6 NM | 45000ft |  | 
HK |  |  |  |  |  | 
RT |  | Rapier |  |  |  | 
A | ZSU |  |  |  |  | AAA
DE | Sborka | Dog Ear |  |  |  | 
 | EWR |  |  |  |  | 
 | EWR |  |  |  |  | 
 | SA-9 |  |  |  | 3 | IR
 | SA-18 |  |  |  | 3 | IR
NOT UPDATED for VIPER

## Slide 48: Template format: SCRAMBLE
This is________ with an ___________SCRAMBLE
For_________, Time is ____Z, I authenticate____
Scramble___________, ______ x ____________
Vector__________, at _________________
Proceed to__________________________
Contact_______ On___________ Backup_______
(QRA/CAS/AR/CSAR)
(Controlling Agency)
Airbase
Flightevel or Feet
Course
Flight callsign
Number
Type of AC
Time
Area/Coordinates/Killbox/Location
C2 Agency
Frequency
Frequency
Remarks:_________________________________________

## Slide 49: Risk Estimate Distances (RED)
Weapon | Description | 0,1 % PI
MK-82 contact | 500 Ib bomb | 300m
MK82 HD contact | 500 Ib bomb/ high-drag | 300m
MK84 contact | 2000 Ib | 350m
CBU-87 | Cluster | 350m
CBU-103 | Cluster | 300m
GBU-12 | 500 Ib Laser Guided | 200m
GBU-10 | 2000 Ib Laser Guided | 250m
GBU-38 | 500 Ib JDAM | 200m
GBU-31 | 2000 Ib JDAM | 250m
AGM-65 | Maverick 125 Ib warhead | 150m
M151, M229, M261 | 2.75" Rockets medium altitude | 250m
M151, M229, M261 | 2.75" Rockets low altitude | 300m
GAU-8 | 30mm Gatling gun | 75m
2A42 | 30mm KA-50 | 75m
UPK 23-250 | 23mm Gunpod KA50 | 50m
S-8 | 80mm Rocket KA-50 | 200m
S-13 OF | 122mm Rocket KA50 | 250m
9K121 VIKHR | 130mm Missile KA50 | 100m
KH-25ML | 275mm Missile KA50 | 175m
M134 Minigun | 7.62X51 gatling UH-1 | 50m

## Slide 50: Collateral Damage Estimate (CAS/AR)
CDE LEVEL | EFFECT | APPROVAL AUTHORITY | RESTRICTION
CDE 1 | High collateral damage expected -More than 20 civilian casualties -Nuclear/chemical/biological spillout expected | AOC/AWACS | CDW TLE CAT 1 coordinates
CDE 2 | Collateral damage expected -Between 5-20 civilian casualties | AOC/ AWACS/JTAC/ | PGM TLE CAT 1 or 2 coordinates
CDE 3 | Collateral damage risk. -CD object within 200m from target | AOC/AWACS/ JTAC/FAC(A)/ SCAR | PGM
CDE 4 | Minor collateral damage risk. -CD object within 500m from target | AOC/AWACS/ JTAC/FAC(A)/ SCAR/ Flight | Weaponeering: No CD object within RED
CDE 5 | No risk of collateral damage | AOC/AWACS/ JTAC/FAC(A)/ SCAR/ Flight/Individual pilot | None
NOT UPDATED for TRM or OPUF
Notes: Collateral Damage Estimates are only valid during CAS operations and AR operations.
In self-defense these do not apply, however the Law of Armed Conflict is in effect, target must satisfise the three criteria :
Distinction: Only engage military objectives. Do not attack civilians or civilian objects.
Proportionality: When engaging military objectives, ensure that expected collateral damage is not excessive to the expected military advantage
Military necessity: an attack or action must be intended to help in the defeat of the enemy

## Slide 51: Target Location Error Catgory (TLE)
TLE CAT 1 | TLE CAT 2 | TLE CAT 3 | TLE CAT 4 | TLE CAT 5 | TLE CAT 6
0-6m | 7-15m | 16-30m | 31-91m | 92-305m | Above 305m